## Slide 1
WEEKLY LAB UPDATE
SLAVV Python exact-route progress
May 26-Jun 14, 2026
One sentence
We turned MATLAB parity from an open debugging effort into a staged proof, and removed key blockers to running that proof at canonical scale.
0/0
target per proof stage
Done
crop energy gate
Pending
canonical sequence
Boundary
This is progress toward Phase 1 certification, not a final certification claim.
SLAVV Python update | May 26-Jun 14, 2026

## Slide 2
CLAIM BOUNDARY
The bar is strict stage equality
Old framing
Match rates were useful for debugging, but they were not a certification standard.
Current bar
Energy, Vertices, Edges, and Network each need zero missing and zero extra.
Later claim
Paper-profile ship confidence is Phase 2.
Phase 1 = exact-route certification on full 180709_E.
No percentage exit
No oracle vertex injection
No final claim yet
SLAVV Python update | May 26-Jun 14, 2026

## Slide 3
WORK COMPLETED
Four changes made the proof workflow real
Pipeline
Resumable run state and cleaner stage managers for Energy through Network.
Proof harness
Sequential prove-exact gates, crop/canonical pre-gates, and MATLAB oracle promotion.
Operations
Detached parity jobs plus monitor/status commands for long Windows runs.
Docs
One task hub, one live findings log, and one Phase 1 spec.
Net effect: the next failure should point to a specific stage, not a vague project state.
SLAVV Python update | May 26-Jun 14, 2026

## Slide 4
BLOCKERS REMOVED
Canonical Energy can now run for the right reason
>400 MB
saved per chunk by sparse meshes
~30x
lower peak energy stack
float64
systemic precision alignment
Y/X/Z
MATLAB grid alignment
F-order
tie-break parity
Memory
Sparse meshes, incremental best-scale updates, FFT cleanup, and Bessel chunking reduce OOM risk.
Numerics
float64, MATLAB-style rounding, and mesh phase alignment prevent branch drift.
Indexing
Internal Y/X/Z with Fortran order matches MATLAB tie-breaking.
These fixes do not prove Phase 1; they make the proof runnable and fair.
SLAVV Python update | May 26-Jun 14, 2026

## Slide 5
CURRENT STATUS
One gate closed; the sequence remains open
Gate
State
Meaning
Crop Energy
DONE
Bit-perfect after float64 and axis/shift fixes.
Crop Vertices
PENDING
Prove after refreshed exact-route checkpoints.
Crop Edges
PENDING
Depends on matching vertices.
Canonical Energy
PENDING
Resume phase1_cert_network with memory-safe path.
Canonical Sequence
PENDING
Final full-volume Energy -> Network proof.
Context
v29 edges reached 88.7% pair match; that is a diagnostic baseline only.
Exit
All four canonical stages must pass strict zero on one run root.
SLAVV Python update | May 26-Jun 14, 2026

## Slide 6
NEXT STEPS
Short path from here
1
Refresh crop checkpoints
Run exact route through vertices, edges, and network.
2
Prove crop sequence
Stop at the first failing stage.
3
Resume canonical Energy
Use the memory-safe phase1_cert_network path.
4
Promote only strict-zero proof
Record Phase 1 after all canonical gates pass.
Bottom line: the work made certification concrete and runnable. The certification itself is still pending.
SLAVV Python update | May 26-Jun 14, 2026